PRACTICAL EXERCISE

| Title | SINCGARS SECURE SINGLE CHANNEL OPERATIONS |
| --- | --- |
| Introduction | This practical exercise will provide you with the guidance necessary to operate a SINCGARS in the secure single channel mode. Your training objective is to practice hands-on operation until you are able to establish secure single channel communications (usually within 3 minutes, 5 min for MANPACK). |
| Terminal Learning Objective | Note: Inform the student of the following terminal learning objective requirements: |
|  | At the completion of this lesson you (the student) will: |
|  | Action: | Operate a SINCGARS in the secure single channel mode. |
|  | Condition: | Given an assembled tactical radio (SINCGARS MANPACK) with a SOI, KYK-13 with TEK and fill cable; ACP 125(E) and U.S. Supplement-1, FM 24-18, FM 24-19, TM 11-5820-890-10-1, and TM 11-5820-890-10-8; 101-31U/Job Aid 1; preloaded COMSEC; an operational distant tactical radio/network (compatible to the radio being trained), and the Student Information Sheet/Reading assignment. |
|  | Standard: | Establish secure single channel voice communications (usually within 3 minutes, 5 min for MANPACK) with a distant station. |
| Safety Requirements | 1. Lithium batteries are flammable; toxic gases could cause harmful side effects (References: 40 Code of Federal Regulations (pert #262), and TB 43-0134, Battery Disposition and Disposal). 2. The MANPACK antenna extends 1 foot above the radio set, therefore, there is a possibility of eye injury. |
| Risk Assessment Level | This PE is assigned a risk assessment level of LOW |

| Environmental Considerations | None |
| --- | --- |
| Evaluation | Successfully complete all steps within this practical exercise. |
| Instructional Lead-in | This practical exercise directs you in the practice of operating SINCGARS in the secure single channel mode. The primary aid is Job Aid 1. |
| Resource Requirements | SINCGARS with TM 11-5820-890-10-1, Chapter 2, pg 2-33; KYK-13 with TEK and fill cable; Frequency and call signs. |
| Special Instructions | Complete the reading assignment/Student Information Sheet. Check your work position and make sure that you have the required resources. If any are missing, notify your instructor. |
| Procedures | Review procedures provided in the Student Information Sheet and Job Aid. The Practical Exercise is complete when communications with the distant end is established. |
| Feedback Requirements | Schedule and provide feedback on any information to help answer inquiries about the task. |
|  | Note: Rapid, immediate feedback is essential to effective learning. |