Request Medical Evacuation

081-831-0101

Conditions: You have a casualty requiring medical evacuation (MEDEVAC) and you will need a patient pickup site. You will need operational communications equipment, MEDEVAC request format, and unit signal operation instructions (SOI).

Standards: Transmit a MEDEVAC request, providing all necessary information as quickly as possible. Transmit, as a minimum, line numbers 1 through 5 during the initial contact with the evacuation unit. Transmit lines 6 through 9 while the aircraft or vehicle is en route, if not included during the initial contact.

Performance Steps

1. Collect all applicable information needed for the MEDEVAC request.

a. Determine the grid coordinates for the pickup site. (See STP 21-1-SMCT, task 071-329-1002.)

b. Obtain radio frequency, call sign, and suffix.

c. Obtain the number of patients and precedence.

d. Determine the type of special equipment required.

e. Determine the number and type (litter or ambulatory) of patients.

f. Determine the security of the pickup site.

g. Determine how the pickup site will be marked.

h. Determine patient nationality and status.

i. Obtain pickup site chemical, biological, radiological, and nuclear (CBRN) contamination information normally obtained from the senior person or medic.

Note: CBRN line 9 information is only included when contamination exists.

2. Record the gathered MEDEVAC information using the authorized brevity codes. (See table 081-831-0101-1.)

Note: Unless the MEDEVAC information is transmitted over secure communication systems, it must be encrypted, except as noted in step 3b(1).

a. Location of the pickup site (line 1).

b. Radio frequency, call sign, and suffix (line 2).

c. Numbers of patients by precedence (line 3).

d. Special equipment required (line 4).

e. Number of patients by type (line 5).

f. Security of the pickup site (line 6).

g. Method of marking the pickup site (line 7).

h. Patient nationality and status (line 8).

i. CBRN contamination (line 9).

3. Transmit the MEDEVAC request. (See STP 21-1-SMCT, task 113-571-1022.)

a. Contact the unit that controls the evacuation assets.

(1) Make proper contact with the intended receiver.

(2) Use effective call sign and frequency assignments from the SOI.

(3) Give the following in the clear "I HAVE A MEDEVAC REQUEST;" wait one to three seconds for a response. If no response, repeat the statement.

b. Transmit the MEDEVAC information in the proper sequence.

(1) State all line item numbers in clear text. The call sign and suffix (if needed) in line 2 may be transmitted in the clear.

Note: Line numbers 1 through 5 must always be transmitted during the initial contact with the evacuation unit. Lines 6 through 9 may be transmitted while the aircraft or vehicle is en route.

(2) Follow the procedure provided in the explanation column of the MEDEVAC request format to transmit other required information.

(3) Pronounce letters and numbers according to appropriate radiotelephone procedures.

(4) End the transmission by stating "OVER."

(5) Keep the radio on and listen for additional instructions or contact from the evacuation unit.

Table 081-831-0101-1 MEDEVAC Request Format "c:\\asat\\asat_036\\036_157.doc" Table 081-831-0101-1 MEDEVAC Request Format (cont) "c:\\asat\\asat_036\\036_977.doc"

Evaluation Preparation: 
Setup: Evaluate this task during a training exercise involving a MEDEVAC aircraft or vehicle, or simulate it by creating a scenario and providing the information as the Soldier requests it. You or an assistant will act as the radio contact at the evacuation unit during "transmission" of the request. Give a copy of the MEDEVAC request format to the Soldier.

Brief Soldier: Tell the Soldier to prepare and transmit a MEDEVAC request. State that the communication net is secure.

| Performance Measures | GO | NO-GO |
| --- | --- | --- |
| 1. Collected all information needed for the MEDEVAC request line items 1 through 9. | —— | —— |
| 2. Recorded the information using the authorized brevity codes. | —— | —— |
| 3. Transmitted the MEDEVAC request as quickly as possible, following appropriate radiotelephone procedures. | —— | —— |

Evaluation Guidance: Score the Soldier GO if all performance measures are passed. Score the Soldier NO GO if any performance measure is failed. If the Soldier scores NO GO, show what was done wrong and how to do it correctly.

| References |
| --- |
| Required | Related |
| None | FM 4-02.2 |
|  | STP 21-1-SMCT |